| Measurement | Definition | Method of Measuring | Data Sheet Column |
| --- | --- | --- | --- |
| Span: (Sculling) | The distance between the Centre of the Pins at the point of attachment to the rigger | Measuring Tape | M |
| Spread: (Sweep) | Shortest distance from the mid line of the boat to the Centre of the Pin at the point of attachment to the rigger. | Precision tool/ measuring tape | N |
| Oar/Scull Length Overall: | Overall Length of the Shaft and Blade measured to the end of the blade in a straight line with the shaft. | A measuring tape | O |
| Oar/Scull Length Outboard: | Derived from the Overall Oar/Scull Length minus the Inboard Length | A measuring tape | P |
| Gearing | Rowing the outboard divided by the spread. Sculling the outboard divided by half the span | Calculation Sculling: outboard divided by Half (span minus swivel width) Sweep: outboard divided by (spread minus ½ swivel width) | Q |
| Oar/Scull Length Inboard: | The distance from the end of the handle to the Side of the Collar that rests against the Swivel. | A measuring tape | R |
| Overlap: (Sweep) | The amount by which the Oar Handle extends beyond the Centre Line of the Boat at the orthogonal position | Calculation: (Inboard Length minus Spread) + Half the Swivel Width. (Normally 2 cms). | S |
| Overlap: (Sculling) | The amount by which both Sculls Overlap each other in the orthogonal position. | Calculation: {(Inboard Length x 2) minus Span} +, (2 x Half the Swivel Width). (Normally 2 cms). | S |
| Blade Length: | The Length of the Blade from the connection with the shaft of the Oar/Scull to the Tip of the Blade in a straight line with the Shaft. | A measuring tape | T |
| Line of work: (The 'rowing face' of the Swivel) | A Line across the boat level with the 'Face' of the Swivel. | Sculling: a rectangular metal bar fixed firmly to the face of both swivels. Position measured and marked using a set square Rowing: similar but ensuring the swivel is at 90% to the mid line of the boat. |  |
| Distance through the work | The maximum distance beyond the face of the work the front of the seat can travel | A Measuring Tape | W |
| Stretcher Position: (Fore and Aft) | Horizontal distance from the Heel to the Line of Work | Bar across the two saxboards with over the on the saxboard Tool on the saxboard above the Heels to the Centre Line of Work as defined below. | X |
| Stretcher Position: (Fore and Aft) | Horizontal distance from the Toe to the line of work | A Measuring Tape | Y |
| Swivel Height: (Above Seat) | The vertical height of the Swivel above the lowest point of the Stern edge of the Seat. This will be measured 1/3rd of the way along the Sill of the Swivel from the 'rowing' face. | Tool on the saxboard with a measuring device down to the Seat and another up to the Swivel. The addition of these two measurements is the Swivel Height. | AA, AB, AC |
| Stretcher Height: (In relation to Seat) | Vertical distance from the Heel to the lowest point of the Stern Edge of the Seat | Measure vertically down from the saxboard to the heels minus the saxboard down to the seat. | AD |